## Slide 1
Supply Chain Strategy - OSCAR
SELECTED – Existing Suppliers:
None — no pre-qualified ATM supplier for these ION LUNG materials (all sourcing is new; see New / COTS).
SELECTED – New Suppliers:
  Azelis – Proxel BD20 biocide (genuine Arxada; account & credit set up)
  Koch Color – FB 28 disodium salt 4193-55-9 (Opti-Bright BA; sample in progress)
  ChemicalStore – Barium sulfate, precipitated (in stock, 2 lb)
  Amazon (COTS) – Fish gelatin & sodium alginate — current purchase channel
  Modernist Pantry (COTS) – Fish gelatin & sodium alginate — current purchase channel
Existing Suppliers under consideration:
  Sigma-Aldrich / MilliporeSigma – Ruled out for production: now R&D-only for FB 28, Proxel BD20 AND barium sulfate (see Risks).
New Suppliers under consideration:
  Barentz North America – Proxel BD20 (2nd Arxada route) & Venator blanc fixe (BaSO₄)
  Aurora Specialty Chemistries – FB 28 optical brightener (US maker)
  Organic Dyes & Pigments (ORCO) – FB 28 (Synthrowite)
  CIMBAR / Barium & Chemicals – Barium sulfate (US producers)
  Nutra Food Ingredients / Custom Collagen – Fish gelatin (US)
  Ingredion / Roquette (via ChemPoint) – Sodium alginate (US)
Supply Chain Risks:
  Primary supplier gap: Sigma-Aldrich (intended primary) is R&D-only for FB 28, Proxel BD20 AND barium sulfate → full re-sourcing required.
  Single / limited source: FB 28 disodium — few US production makers (Koch Color the cleanest exact match).
  New / unqualified suppliers: most production sources are new to ATM; COA & sample qualification still pending.
  Wrong-material risk: FB 28 free acid (4404-43-7) vs disodium (4193-55-9) mislabeling in catalogs.
  MOQ vs need: production packs (~20–25 kg biocide; ~20 kg Sigma bulk) vs ≤1 kg requirement.
  Capability new to ATM: production-grade optical-brightener & biocide sourcing.
Notes: Amazon & Modernist Pantry are COTS (current purchase channels for gelatin & alginate), not qualified existing suppliers — listed under Selected-New/COTS. No pre-qualified ATM existing supplier for these materials. Sigma-Aldrich ruled out for production (R&D-only for FB 28, Proxel BD20 and barium sulfate). Data as of Aug 2026.